## Slide 1
Programmer's view on Computer Architecture
by Istvan Haller

## Slide 2: Basic purpose of a processor (CPU)
Perform computations between data

## Slide 3: Addition of a feed-back loop
Temporary storage to reuse computations

## Slide 4: Registers
Registers allow reuse of computations
Efficiency ↔ Keep data on processor
Uniquely addressable by name
Multiple types
  General purpose: managed explicitly by program
  Special purpose: implicit usage
    Some can be accesses explicitly as-well

## Slide 5: Set up and forget → Memory
Minimize user interaction through storage

## Slide 6: Content of memory
Commands to be executed (instructions)
Input data ← What does the application need?
Output data ← Final result of computations
Temporary data ← Registers are limited

## Slide 7: Accessing memory
Memory is contiguous string of bytes
  No structure!!!
  Structure is defined through usage
Access based on address ← Offset in memory
Can be both read or written

## Slide 8: Instructions in memory
Components of an instruction:
  Command to be executed
  Registers to be used
  Numeric constants (including memory addresses)
Instructions executed in sequence
  Address generated by Program Counter

## Slide 9: Accessing data in memory
2 main addressing modes
Direct addressing
  Supply the concrete address in memory
    int var1;
    reg1 = load_from (&var1)
Indirect addressing
  Use running computation from register as address
    reg1 = &var1 + 10
    reg2 = load_from (reg1)

## Slide 10: Issues with memory
Can only serve a single request at a time
Requirements to process instruction:
  Read instruction from memory (always)
  Read/write any memory operands (typically)
Limit number of memory operands
  X86: maximum 1 memory operand
  Simple processors (ARM): no memory operands
    Special memory manipulation instructions: load, store

## Slide 11: Memory organization: Harvard
Simplest design, inefficient memory usage

## Slide 12: Memory organization: Neumann
Traditional design, contention for memory

## Slide 13: Memory organization: current
Single memory, but separation of access

## Slide 14: Changing the program flow
Until now we considered sequential order
What happens for the following construction?
    if (cond)
    codeA;
    else
    codeB;
PC needs to change based on conditional
New sources for PC value

## Slide 15: Influences on Program Counter
Jumping: non-sequential change in PC
Relative jump ↔ Skip block of code
Absolute jump ↔ Go to specific line of code

## Slide 16: Conditionals
Evaluate conditional → Change program flow
    if (a < b)
Components:
  Operands “a” and “b”
  Operation “<”
  Jump targets (what should happen with PC)
Too much for single instruction

## Slide 17: Evaluator vs Conditional Jump
Separate evaluation from program flow
Evaluator: instruction that compares operands
  Similar to arithmetic and logic instructions
  Result is binary flag (True/False)
Propagate result to conditional jump
  Change program flow based on state of flag
Compare(“<”, a, b)→Flag Register→Flag ? Target1 : Target2

## Slide 18: Conditional jump
Two targets too much for single instruction
Implicit target is next instruction
  Fall-through edge
Pseudo-code interpretation
    if (cond)
    goto explicit_target;
    implicit_target:
    …
    explicit_target:

## Slide 19: Restructuring conditional code

## Slide 20: Restructuring conditional code

## Slide 21: Restructuring conditional code

## Slide 22: Restructuring conditional code

## Slide 23: Restructuring conditional code

## Slide 24: Supporting function calls
What is a function call?
  Start executing function code↔Jump to function
  Return to caller location↔Jump back to call site
But where was the function called from?
Store return address when calling function
  Multiple functions in program!
  Function may be called multiple times (re-entrant)!
  Need for designated storage

## Slide 25: Function call in a nut-shell

## Slide 26: Managing the return address

## Slide 27: Managing the return address

## Slide 28: Managing the return address

## Slide 29: Managing the return address

## Slide 30: Managing the return address

## Slide 31: The stack!
Last return address stored used by first return
Last In – First Out ↔ Stack
Stack Requirements:
  Contiguous sequence of memory
  Stack Pointer ← Special Purpose Register

## Slide 32: Other function related concepts
Function arguments
  Unique for every instance of the function call
  Passed in registers?
    Possible if no other functions called
    Otherwise registers need to be saved (where?)
  Typically passed on the stack
    Instance specific storage as with return address
    No limit on argument count (variable length possible)

## Slide 33: Other function related concepts
Function local variables
  Similar to function arguments
  Unique for every instance of the function call
Temporary storage of registers
  Function execution may be interrupted
  Need to save registers in the function context
  Use the stack as “unlimited” storage

## Slide 34: Function frames
Elements related to given function instance
  Arguments, return address, locals, temporaries
Stack pointer volatile inside function
How to find beginning of function frame?
  Base Pointer Register
What about the previous function?
  Store chain of base pointers on stack