## Slide 1
Interacting with X86 hardware devices
by Istvan Haller

## Slide 2: Topics to be discussed
Demo: Real-time clock with interrupts
  Managing interrupt handlers
  Description of the real-time clock
  Step-by-step code development
Description of other hardware devices
  Keyboard, Timer, Soundcard
Mini-project ideas
  Description + overview of development

## Slide 3: Demo: Real-time clock with interrupts
Purpose
  Learning interrupt handling on real example
  Understanding hardware specifications
    From online wiki or official programmer’s guide
  Writing cool assembly programs
Questions?
  What is the real-time clock and how do you use it?
  How do I install my interrupt handler?

## Slide 4: Installing interrupt handlers
Handlers installed into interrupt descriptor table
IDT contains an entry for every interrupt
CPU accesses IDT indexed on interrupt number
IDT located anywhere in memory
Special CPU register (IDTR) holds info of IDT
Disable interrupts while manipulating IDT!
  Disable: CLI; Enable: STI
OSDev IDT info

## Slide 5: Manipulating the IDT
Structure of IDTR (on 64bit)
  10 bytes long (2 + 8)
  Offset 0, Size 2: Maximum offset in IDT (in bytes)
    Size of IDT – 1
  Offset 2, Size 8: Address of IDT in memory
Reading the value of IDTR: SIDT [address]
Write IDTR using bytes from memory
  LIDT [address]

## Slide 6: Entry in IDT (64bit architecture)
Each entry is 16 bytes long
  Offset 0, Size 2: Address low bits (0..15)
  Offset 2, Size 2: Code segment selector
  Offset 4, Size 1: Zero
  Offset 5, Size 1: Type and Attributes
  Offset 6, Size 2: Address middle bits (16..31)
  Offset 8, Size 4: Address high bits (32..63)
  Offset 12, Size 4: Zero

## Slide 7: From request to interrupt
Each hardware device has dedicated IRQ wire
CPU cannot have unlimited input
CPU only interested in interrupt number (vector)
Solution: interrupt controller
  Handles individual interrupt requests
  Only communicates interrupt number to CPU

## Slide 8: Interrupt Controller
Mapping event on physical wire to interrupt
Handling simultaneous events
Why not have dynamic mapping?
  Extensibility of hardware devices
  Separation between software and hardware design
Programmable Interrupt Controller
  Configurable mapping at run-time
  Configurable priority levels for interrupts

## Slide 9: Programmable Interrupt Controller

## Slide 10: Programmable Interrupt Controller

## Slide 11: Advanced PIC (APIC) architecture

## Slide 12: Demo V1: Software interrupt
Write a custom interrupt handler
Trigger handler using software interrupt
Avoid hardware interaction at first
Baseline:
  Write “Hello world!” to the screen after interrupt

## Slide 13: V1: Create interrupt handler
Avoid complex processing in handler
Set flag when handler executes
custom_interrupt_handler:
mov byte [FLAG], 1
iretq

## Slide 14: V1: Install interrupt handler
Compute address of IDT entry 20 using IDTR
cli ; Disable interrupts
sidt [IDTR] ; Store value of IDTR to memory
lea rbx, [IDTR + 2] ; Select offset from IDTR
mov rbx, [rbx] ; Read offset of IDT into RBX
lea rbx, [rbx + 16 * 20] ; Address of IDT entry 20

## Slide 15: V1: Install interrupt handler
Save address of handler in selected entry
lea rax, [custom_interrupt_handler] ; Address
mov [rbx], ax ; Store lower 16 bits
shr rax, 16 ; Store next 16 bits
mov [rbx + 6], ax
shr rax, 16 ; Store remaining 32 bits
mov [rbx + 8], eax
sti ; Enable interrupts

## Slide 16: V1: Main loop
Main typically performs background processing
Infinite loop waiting for signal from handler
loop: xor rax, rax ; Check value of FLAG
mov al, [FLAG]
test al, al
jz loop ; Loop while value is 0

## Slide 17: V1: Result of trigger
Print “Hello world!” when signal detected
Loop terminates and print called
mov rsi, hello_message ; Load RSI with string call b_print_string ; Print the string

## Slide 18: V1: Trigger software interrupt
Needs to occur before infinite loop
Not needed when hardware devices are involved
int 20 ; Trigger interrupt 20

## Slide 19: Demo V1: Evaluation
String printed every time
Works even after multiple executions
Everything seems to be perfect

## Slide 20: Demo V2: Real-time clock
Use a real hardware event as source of interrupt
Real-time clock also used by OS components
Make sure system is not broken by application
Learn about hardware interaction

## Slide 21: Interacting with hardware
Connected with CPU through “ports”
Each includes Control/Status registers
  Small piece of storage local to hardware device
Interaction protocol hardware specific
  Typically described in data sheet
  Few patterns in practice

## Slide 22: Reading/Writing hardware ports
Ports accessed though dedicated instructions
  IN dst, port_number
  OUT port_number, src
For 8-bit ports
  port_number: immediate or DX register
  src/dst: AL
For 16-bit ports: DX and AX
Some ports are also memory mapped

## Slide 23: Real-time clock (RTC)
Low frequency clock chip for keeping time
Operates at 32kHz
  Theoretically adjustable, but it affects time-keeping
Secondary frequency provided using divider
  2Hz – 32KHz: “real-time” frequencies
  frequency = 32768 >> (rate-1);
Secondary frequency generates interrupts (IRQ 8)

## Slide 24: Configuring the RTC
2 stage write
  Write target register index to port 70h
  Read/Write data to target register through port 71h
Status Register A: index Ah
  Bit 7: Update in Progress flag, inconsistent date
  Bits 6-4: Frequency configuration, don’t modify
  Bits 3-0: Rate configuration (1111b: 2Hz, 1110b: 4Hz, ..)
ICH10 Datasheet – page 439
OSDev RTC usage

## Slide 25: Additional RTC features
Integrated with CMOS for time/date storage
  Runs on battery when system shut down
Ability to retrieve in-depth date information
  Seconds/Minutes/Hours
  Day/Month/Year
  Weekday
Additional status/control information
  Status Register B and C
OSDev CMOS info

## Slide 26: V2: Interrupt source change
IRQ 8 mapped to entry 28h by kernel
lea rbx, [rbx + 16 * 28h] ; Address of RTC entry
No more software interrupt call

## Slide 27: Demo V2: Evaluation
String printed on first execution
System freezes
Virtual LEDs stop blinking
Did RTC stop after first interrupt?
Did we break the OS?
Needs more debugging!

## Slide 28: Demo V3: Multiple interrupts
Require multiple handler executions before print
Checks that RTC generates periodic interrupts
Use counter in handler to monitor execution count
Only set flag, when counter reaches 8

## Slide 29: V3: New handler
custom_interrupt_handler:
inc byte [COUNT]
cmp byte [COUNT], 8
jne end_custom_interrupt_handler
mov byte [FLAG], 1
end_custom_interrupt_handler:
iretq

## Slide 30: Demo V3: Evaluation
String never gets printed
Interrupt handler does not trigger 8 times!
Possibly interrupt occurs a single time!
Reasons?
Detailed hardware specifications (OSDev):
  “If register C is not read after an IRQ 8, then the interrupt will not happen again”
  “The PIC doesn't send any more interrupts until the cpu acknowledges the interrupt.”

## Slide 31: Demo V4: Extended handler
Look into OS code to extend handler
Apply code fragments to custom handler
2 components:
  Reading Status Register C of RTC
  Acknowledge interrupt on LocalAPIC
    LocalAPIC is memory mapped
    Address of LocalAPIC is stored in bootloader infomap

## Slide 32: V4: Read address of LocalAPIC
Taken from OS code
; Read the address from the Pure64 infomap
mov rsi, 5060h ; Location in infomap
lodsq ; Read quad-word from [rsi] to rax
mov [LOCAL_APIC], rax

## Slide 33: V4: Extend end of handler
mov al, 0Ch ; Select RTC register C
out 70h, al ; Port 70h is the RTC index
in al, 71h ; Read the value in register C
; Acknowledge the IRQ
mov rsi, [LOCAL_APIC]
xor eax, eax
mov dword [rsi + 0B0h], eax

## Slide 34: Demo V4: Evaluation
String printed to screen
Interrupt triggered multiple times!
Execution freezes when application terminates
Some OS components dependent on RTC?
Further extension of handler counter-intuitive

## Slide 35: Demo V5: Chained interrupts
Old interrupt handler contains required code
Old interrupt handler compatible with OS
Chain interrupt handlers
  Jump to old handler instead of IRET
  Old handler will perform necessary IRET
  Jump instead of call ← No reason to return
  Similar to “Tail-call” optimization in compilers

## Slide 36: V5: Read address of old handler
mov eax, [rbx + 8] ; Load upper 32 bits
shl rax, 32
mov ax, [rbx + 6] ; Load next 16 bits
shl rax, 16
mov ax, [rbx] ; Load remaining 16 bits
mov [ORIGINAL_HANDLER], rax

## Slide 37: V5: Chain handlers
custom_interrupt_handler:
inc byte [COUNT]
cmp byte [COUNT], 8
jne end_custom_interrupt_handler
mov byte [FLAG], 1
end_custom_interrupt_handler:
jmp [ORIGINAL_HANDLER]

## Slide 38: Demo V5: Evaluation
Works the first time
Virtual LEDs continue to work
Freezes when executed a second time
What happens on second execution?
  IDT still points to custom handler
  Handler loops to itself

## Slide 39: Demo V6: Proper clean-up
Handlers need to be restored before termination
No guarantees about code left in memory
No reason to maintain unneeded handler
Same code as the one writing custom handler

## Slide 40: Demo V6: Evaluation
String printed every time
Works even after multiple executions
Everything seems to be perfect

## Slide 41: Demo V7: Modularization
Code installing handler written twice in code
Why not encapsulate it in a function?
Which calling convention to use?
  Small internal code
  Just use some registers
  Clearly document custom calling convention!
  Be careful about locally used registers!

## Slide 42: V7: Function installing handlers
; Installs a new interrupt handler
; RCX interrupt ID (16 bit)
; RAX address of new handler
; RDX memory location to store old handler
install_interrupt_handler:
push rax ; Save rax
…
pop rax ; Restore rax

## Slide 43: Demo V8: Custom frequency
What is the current rate of interrupts?
  Kernel configures RTC secondary frequency to 8Hz
Can we reconfigure it? Sure!
Write new configuration to Status Register A

## Slide 44: V8: Configuring Status Register A
mov al, 0Ah ; Select Status Register A
out 70h, al
in al, 71h ; Read current content
and al, 0F0h ; Preserve upper 4 bits of AL
or al, 1111b ; Set RTC rate to 2Hz
out 71h, al ; Write new content

## Slide 45: Demo V8: Evaluation
Everything still works as expected
String printed after a longer time (4 seconds)
Virtual LEDs blink at a slower pace
  Even after application terminates
Applications may depend on given frequency
  Need to restore frequency before termination

## Slide 46: Demo V9: Full clean-up
Ensure that frequency configuration restored
Create function for RTC configuration
Save old configuration to memory
Similar to the interrupt handler clean-up

## Slide 47: Demo V9: Evaluation
Everything works as expected
Virtual LEDs blink at a slower paced
  Blink speed restored after application finishes
Demo finished!
Conclusions:
  Carefully read hardware specification
  Think about the different system interactions
  Develop applications step-by-step

## Slide 48: Other hardware devices: Keyboard
Accessed through PS/2 controller
  USB legacy support on motherboard
2 IO Ports: Data and Status/Command
  60h: Data (both read and write)
  Read mode of 64h: Status
  Write mode of 64h: Command
Interrupts generated on IRQ1 (IDT entry 21h)
OSDev PS/2 usage

## Slide 49: Other hardware devices: Keyboard
Managing data from keyboard:
  Information received in the form of scan-codes
  Scan-code represents physical action on keyboard
  State managed in software (Shift, Alt, keys held down)
Commands:
  Set keyboard LED status
  Configure keyboard behavior
OSDev Keyboard usage

## Slide 50: Other hardware devices: Timers
Timers are used to measure accurate time delays
Similar to RTC, but finer grained control
Programmable Interval Timer (8253/8254 chip)
  Runs at 1.1931816666 MHz
  Configurable frequency divider
  IRQ0, but APIC not configured in BareMetal
OSDev PIT usage

## Slide 51: Operating principle of Timers

## Slide 52: Other hardware devices: Sound
Different soundcards as PCs evolved
The simplest one to program is SoundBlaster16
  Emulation available in QEMU and VirtualBox
General operating principle applies to any card
  DSP transforms digital information to analog sound
  Manually writing to DSP not preferred
  DMA allows automatic transfer
  DMA interrupt when transfer finishes

## Slide 53: Other hardware devices: Sound
Configuration of SB16 in QEMU
  DMA channel 1
  DMA IRQ5, but APIC not configured in BareMetal
  DSP IO port base address: 220h
Programming the SB16

## Slide 54: Mini-projects: Keylogger
Typically first major assembly project
Requires the understanding multiple components
Requirements:
  Hook keyboard interrupt to intercept keyboard events
  Transform keyboard events into character stream
  Save character stream to disk
  Keylogger runs in background of other application
  Optional: Asynchronous writes to disk

## Slide 55: Mini-projects: Keylogger
Executing in background:
  No multi-process support in BareMetal
  New application reuses memory of old one
  Keylogger needs to stay resident in memory
  Dynamically allocated memory maybe?
Asynchronous disk writes:
  Write to disk in bursts, outside of keyboard interrupt
  Writes triggered by timer maybe?

## Slide 56: Mini-projects: Morse-code app
Fun and visual project
Transform input characters to Morse-code
Display on keyboard LEDs
Requirements:
  Convert keyboard input into Morse-code
  Toggle keyboard LEDs based on code
  Optional: use timers to simplify blink timing
  Optional: hook keyboard interrupts

## Slide 57: Mini-projects: Screen Hack
Introduce screen “hacks” on certain triggers
Different character based animations on screen
  Falling characters (Matrix style)
  Continuously changing characters (color, shape)
Requirements:
  Track certain events (keyboard or timer)
  Runs in background like keylogger
  Manipulates screen buffer in memory

## Slide 58: Mini-projects: Classic game
Develop a classic game like Tetris, Snake, …
Learn to develop a raw graphics engine
Learn to program event-based systems
Requirements:
  Use keyboard interrupts for input events
  Use timers to control game speed
  Develop custom graphics engine

## Slide 59: Mini-projects: Soundcard driver
Develop a real driver based on hardware specs
Play sound using the emulated SoundBlaster16
Requirements:
  Enable the DMA interrupt in the APIC
  Configure the DMA controller and the DSP
  Convert some audio files to the right format
  Optional: Auditory Morse-code
  Optional: Play Audio-CD

## Slide 60: Mini-projects: Serial port daemon
Build a daemon to access the BareMetal API through the serial port
Control BareMetal from host system
Requirements:
  Develop a serial port driver
  Develop a custom communication protocol
  Develop a daemon that executes received commands

## Slide 61: Mini-projects: Multi-tasking
Extend BareMetal with multi-tasking support
Requirements:
  Develop per-process virtual memory support
  Develop data-structures for process information
  Develop support to clone current process (fork)
  Reuse current execution mechanism for “exec”
  Develop a scheduler using timers (preemption)